Computer Structure

Assignment 5

Deadline: 17/3/08 18:00

1. You are given a four bit binary counter. Normally, each clock pulse causes an increment. The counter has a 'clear' synchronic input which clears the counter by the next clock pulse (if clear=1, otherwise the counting proceeds). Add a control input (or some) 'S' which determines the final count of the counter. That is, the counting

will be : 0,1,2,,,,S,0,1,2,,,S,...

Use minimum number of gates.

2. Construct a mod-6 counter using one mod-2 counter, one mod-3 counter and minimum number of gates.

No additional memory devices (FF/registers/counters) allowed.

3. Design a serial subtractor for two 4-bit numbers using ONE FULL ADDER. The numbers are in the range (-8) -(+7) (i.e. 2's complement). Use SHIFT REGISTERS, FLIP-FLOPS and minimal logic as necessary.

Please notice that the answer is in the range of (-15) - (+15).

Hint - find a serial negator for a 2's complement number.

4. Design a synchronic detector (גלאי) for the two series: 0101, 1011. Overlapping (חפיפות) is not permitted.

Use D-FF units and gates in a minimal manner.

5. The following synchronic system, which contains one unit of JK-FF, is given

J=x1x2 , K=(x1+x2)' , z= (x1)XOR(x2)XOR(y)

(The system also has an AND gate, NOR gate and XOR gate).

x1 and x2 are the system's inputs and z is the output.

- Find the state table of the system.

- Obtain the state diagram.

- Determine the function of the system.

(y represents the present state of the flip flop )

6.

שאלה ממבחן תשס"ו מועד ב'

עליכם לבנות מערכת סינכרונית אשר מכילה מספר שלם וחיובי. בכל מחזור שעון המערכת מקבלת מספר בינארי חיובי בן שתי סיביות מבין - 01,10,11 - אשר מוכפל במספר שמוכל במערכת. המערכת שומרת את המספר החדש (אחרי ההכפלה).  ערכו ההתחלתי של המספר השמור במערכת הוא 1.

על המערכת להדפיס 1 אם המספר השמור במערכת מתחלק ב-3 עם שארית 1.

דוגמה:

זמן                        קלט נוכחי                     פלט נוכחי

1                               01                                   1

2                               10                                   0

3                               10                                  1

- (5 נק')  שרטטו את דיאגרמת המצבים בעלת מספר המצבים המינימלי של המערכת. עליכם לצמצם את המכונה או לתת נימוק מדוע היא לא מצריכה צמצום.

- (7 נק') בנו את טבלת המעברים ואת טבלת המימוש הלוגי בעזרת דלגלגים מסוג T  .

- (8 נק') רשמו את משוואות הקלטים לכל  FF ואת משוואת הפלט. אין צורך לצייר את המעגל.