## Slide 1: Information Security – Theory vs. Reality 0368-4474, Winter 2015-2016 Lecture 9: Leakage resilience (continued)
Lecturer: Eran Tromer

## Slide 2: Leakage resilience (continued)

## Slide 3: Security [Ishai Sahai Wagner ’03]
black box
indistinguishable
admissible leakage/ tampering
adversary
simulator
Adversary chooses a leakage/tampering function, from a given set of admissible leakage/tampering functions, to be applied to the wires.

## Slide 4
INPUT
OUTPUT
CIRCUIT
MEMORY
Security definition
Transformer protects privacy (of the initial state) against a given class of admissible leakage/tampering: circuit C efficient Sim admissible Adv initial state s0 : SimAdv,C[s0]  output of Adv attacking C’[s0’] (Even in case of tampering, only privacy is required)
C
INPUT
OUTPUT
CIRCUIT
MEMORY
T
C’
s0
s0’

## Slide 5: Resilient-schemes 1/3 (whiteboard discussion)
Sum-of-wires leakage
  Dual-Rail Logic
Sum-of-wire-transitions leakage
  Dual-Rail Precharge Logic

## Slide 6: Resilient-schemes 2/3 (whiteboard discussion)
Single-wire leakage
  Bit masking or secret sharing
Multiple-wire leakage
  Secret sharing
Leakage of “data-dependent” values from “bulk” computation
  RSA blinding

## Slide 7
t-wire leakage [ISW03]
Secrets additively secret-shared into m=2t+1 shares
Given shares of a=a1 … am and b=b1… bm :
  Compute shares of NOT(a) : apply NOT to a1
  Compute shares ci of a AND b :
    Let zi,j , i<j, be random independent bits
    Let zj,i=(zi,jaibj)  ajbi (i<j)
    Let ci=aibi  ji zi,j
Re-randomize s’ at every iteration (hence m=2t+1).
Security proof sketch: simulator runs adversary and, when asked for leakage value: if answer implied by inputs / inputs / previous answer, answers thus. Otherwise answers randomly. This has the correct distribution.
s0’
Notes: Randomness gates can be eliminated by a random-number generator

## Slide 8: Other leakage?
x
Y
Y
X
black-box
indistinguishable
C’
C
admissible leakage
si

## Slide 9: Our goal
Allow stronger leakage.

## Slide 10: Leakage classes
Locality assumptions
  Single wire, t wires
  Separate sub-circuits
  Leak-free processor: Oblivious RAM [Goldreich Ostrovsky 95]
  Leak-free memory (“only computation leaks information” [Micali Reyzin 04]: leakage is only from CPU state and memory accessed at that program step)
Quantitatively bounded
  Total #bits leaked
  Total #bits leaked per “computational step”
  Noisy leakage from every wire
“Simple leakage”
  Sums and Hamming weights
  Low-complexity global functions
“Too-complicated leakage” (hard to invert)
Some of these are for specific functionality (mainly crypto)
Open problem: realistic models allowing secure and efficient constructions.

## Slide 11: Trusted Computing Architecture (warmup discussion, see next week’s slides)